## Slide 1
Tutorial: Fluent CFD
Eneko Lazpita
ModelFLOWs
Cardiac

## Slide 2
ModelFLOWs
Cardiac
Prof. Michael Neidlin
https://github.com/mneidlin/movingmesh
https://youtu.be/C1O20YvkCJs
https://doi.org/10.5281/zenodo.8233365 https://doi.org/10.1002/eng2.13041

## Slide 3
ModelFLOWs
Cardiac
Step 0: Prerequisites
Python and Spyder: install pip, numpy wheel, matplotlib, scipy.
Ansys Workbench, SpaceClaim, Meshing, Fluent, CFD-Post
STL files of the ventricle evolution. (Go to Geometry Preprocessing tutorial)
Step 0.1: Load given workbench file
Setup of this tutorial done.
Very important to avoid negative volumes when loading mesh.

## Slide 4
ModelFLOWs
Cardiac
Geometry & Mesh
Step 1.1: Load Geometry
Reset Geometry
Open SpaceClaim
Load initial geometry using Assembly  File  ventricle_0.stl
Make sure you set the STL units in the correct one for your geometry when loading (milimeters in ours)
Right click in Facets  Convert to solid  Do not merge faces

## Slide 5
ModelFLOWs
Cardiac
Geometry & Mesh
Step 1.2: Meshing
Update Upstream Components and Edit mesh.
Define Boundaries with Named Selections: Inlet, Outlet, Ventricle.
Define Element Size as your mesh base size.
Tetrahedron  Patch Comforming Method necessary for our setup.
(Optional) Inflation: To include prism layers (Post meshing necessary).

## Slide 6
ModelFLOWs
Cardiac
Simulation Setup
Step 2.1: Loading User Defined Functions
Start Fluent: Double precision and desired processes.
Change solver processes: Parameters & Customization  User-defined Memory
Check and adjust the zone IDs of the outer walls (here: Inlet, outlet and wall-ventricle) in the UDF (udf_exPts.c)
Parameters & Customization  User Defined Functions  Manage
  Unload libudf
Copy Necessary Files to Fluent directory
Parameters & Customization  User Defined Functions  Compiled
  Add... (udf_exeDynMesh.c; edf_exPts.c; BC_profiles.c)
  Use Built-In Compiler  Build  Load
Parallel  Partition/Load Balance  Dynamic Mesh

## Slide 7
ModelFLOWs
Cardiac
Simulation Setup
Step 2.2: Setup
General: Pressure-Based, Transient
Models: Viscous  Laminar
Material: Fluid  Blood
  Density:
  Viscosity:
Boundary Conditions (initially):
  Inlet: Velocity inlet  udf profile
  Outlet: Wall
  Ventricle-wall: Wall

## Slide 8
ModelFLOWs
Cardiac
Simulation Setup
Step 2.3: Dynamic Mesh
Dynamic Mesh  Smoothing  Settings  Diffusion  Advanced
Dynamic Mesh  Events…
  Read… (dynamic_events)
  Defines the changes at end diastole and end systole.
Dynamic Mesh  Dynamic Mesh Zones  Create/Edit  User-Defined Type for: inlet, outlet, wall-ventricle
  Check if Mesh Motion UDF/Profile: Ven_move::libudf

## Slide 9
ModelFLOWs
Cardiac
Moving Wall
Step 3.1: Assign ID
Parameters & Customization  User Defined Functions  Execute on Demand
  Select First_AssignID::libudf  Execute
  File surface is created in the simulation folder
  Number of nodes for each core are shown in the console

## Slide 10
ModelFLOWs
Cardiac
Moving Wall
Step 3.2: Run ps_detNPts.py
Open “ps_detNPts.py” in Spyder
First execution: Answer Do you need to generate correlation file? Yes: 1. No: 0. with “1”
The reference frame ID is the number of the STL-file in the folder STL, that has been loaded and meshed with ANSYS (0).
Output: Number of Faces and allPtsNum.
First timepoint of cycle as Start FrameID (commonly 0)
Last used timepoint as End FrameID
Code creates surface_% files in a folder PTS

## Slide 11
ModelFLOWs
Cardiac
Moving Wall
Step 3.3: Run ps_intNPts.py
Open “ps_intNPts.py” in Spyder
Set number of STL files on you STL folder as Total number of frames in a cycle
Set number of interpolation steps (to get timesteps for simulation) as Number of intermediate frames
Choose a temporal interpolation method between the frames
Output: number of timesteps for one cycle
Code creates udfsurface_%.asc files in folder UDFPTS  Necessary for mesh movement

## Slide 12
ModelFLOWs
Cardiac
Moving Wall
Step 3.4: Adjust udf_exeDynMesh.c
Parameters & Customization  User Defined Functions  Manage
  Select libudf  Unload
  Delete libudf-folder
Adjust “exeDynMesh.c”
  nTimeSteps: Number of timesteps = maximum index of udfsurface_%.asc (output of “ps_intNPts.py”)
  allPtsNum: Number of all nodes, output of ps_detNPts.py
Compile UDF (see slide 6)

## Slide 13
ModelFLOWs
Cardiac
Run
Step 4.1: Solver Methods & Controls
Solution  Double click on Methods
  Pressure-Velocity Coupling
    Scheme: Coupled
    Flux Type: Rhie-Chow: momentum based
  Spatial Discretization  2nd Order
  Temporal Discretization  2nd Order
Solution  Double click on Controls
  Flow Courant Number: 10
    Approximate based on:

## Slide 14
ModelFLOWs
Cardiac
Run
Step 4.2: Automatic Export
Solution  Double click in Calculation Activities
Automatic Export  Create
  File Type: CGNS
  Select ventricle as Cell Zones.
  Select Quantities: Pressure, Density, Velocity, Vorticity, etc.
  Export Data Every: select export frequency.
  File Name: where to export and name.

## Slide 15
Solution  Double click in Initialization
  Standard Initialization  All zeros
  Initialize
Parameters & Customization  User Defined Functions  Execute on Demand
  Select First_loadMESH::libudf  Execute
Solution  Double click in Run Calculation
  Select Time Step Size: small enough for correct resolution
  Select Number of Time Steps: 5 cycles to see convergence
  Select Max Iterations/Time Steps: enough for internal convergence
Run Calculation  Calculate
ModelFLOWs
Cardiac
Run
Step 4.3: Initialization & Run

## Slide 16
ModelFLOWs
Cardiac
Vortex ring formation, tilting, second smaller ring and outflow
Two swirls in both E and A waves of diastole and outflow in systole
Big recirculation in ventricle center, down to the apex.
Q-Criterion
Vorticity
Velocity

## Slide 17
ModelFLOWs
Cardiac
https://modelflows.github.io/modelflowsapp/cardiacpathologydetection/
Any questions?
Look us up in our website: