## Slide 1
Tutorial: Geometry Pre-Processing
Eneko Lazpita
ModelFLOWs
Cardiac

## Slide 2
ModelFLOWs
Cardiac
Prerequisites:
Matlab with STL management packages.
Open Source software: 3D Slicer, MeshLab, Paraview
CAD Creation Software
CT scan medical data

## Slide 3
Introduction
ModelFLOWs
Cardiac
Ideal
Patient Specific
Construction
Segmentation
STL Generator
Meshing
Simulation
If evolution files available
If evolution files available

## Slide 4
Ideal
ModelFLOWs
Cardiac
Zheng et al., 2012. Computational modeling and analysis of intracardiac flows in simple models of the left ventricle.
Starting Geometry
a: | 2.00 cm | D: | 2.40 cm | C: | 0.55 cm
b: | 8.00 cm | d: | 0.40 cm | c: | 1.35 cm
H: | 4.80 cm |  |  |  | 

## Slide 5
Ideal
ModelFLOWs
Cardiac
Point Classification
Integration
1
1
2
2
3
3
4
4
STL Generation

## Slide 6
Ideal
ModelFLOWs
Cardiac
1. Load Geometry
Read STL file
Scale & extract point and connectivity data
2. Classify Vertices
Detect and categorize vertices based on geometric conditions
3. Process Flow Rate Data
Read flow rate data
Interpolate flow rate data
Adjust flow rates to correct volume differences between systole and diastole.
4. Calculate Volume Variations
Define time steps for STL generation.
Compute volume variations by integrating flow rate chart.
5. Generate STL Files
For each time step:
Calculate scaling factors for the ventricle's dimensions.
Apply displacements to shell & base points based on scaling.
Write new geometry to STL file.
6. Prepare Inlet and Outlet Data
Derive inlet velocities and outlet flow rates from flow data.
Write results to CSV files.

## Slide 7
Patient Specific
ModelFLOWs
Cardiac
MeshLab
ParaView
Segmentation
Pre-Processing
Starting Geometry

## Slide 8
Patient Specific
ModelFLOWs
Cardiac
File  Add Data  Choose File(s) to Add  Select your data
Modules  Converters  Crop Volume:
  Fix
  Check Isotropic spacing
  Spacing scale: 3.00x
  Apply
  Check off Display ROI
Modules  Segmentation  Segment Editor:
  Add: Left Ventricle (we will include aorta & left atrium here), Others
  Paint: Mark seeds in each cavity
  Grow From Seeds: Initialize and Apply
  Click in green arrow “Go to segmentation module”: Create Closed Surface
3D Slicer:

## Slide 9
Patient Specific
ModelFLOWs
Cardiac
3D View (top right panel)  Button of Center View
Fix surface in 3D View: Modules  Segmentation  Segment Editor:
  Paint: Check “Edit 3D”  Fill holes
  Smoothing  Joint smoothing  Apply
Modules  Informatics  Data:
  Right click in Left Ventricle  Export visible segments to models
  Right click in the model created  Export File  Select File Name, Directory and STL format
3D Slicer:

## Slide 10
Patient Specific
ModelFLOWs
Cardiac
File  Import Mesh  Load STL file
Filters  Cleaning and Repairing  Remove Isolated Pieces (wrt Diameter):
  Select the measure percentage: 25.00%
  Apply
Edit  Select Faces in a rectangular region  Select Aorta & Left Atrium
Filters  Selection  Delete Selected Faces
Filters  Cleaning and Repairing  Remove Isolated Pieces (wrt Diameter)
Filters  Remeshing, Simplification and Reconstruction:
  Close Holes  Max size to be closed = 1000  Apply until output is 0 holes
  Remeshing: Isotropic Explicit Remeshing: Apply until smooth mesh
File  Export Mesh As: Save edited STL file
MeshLab:

## Slide 11
Patient Specific
ModelFLOWs
Cardiac
File  Open  Load STL file
Filters  Alphabetical Transform:
  Scale: 0.001 in all directions to have the ventricle in meters
  Rotate: Adjust orientation so z-axis is the vertical direction
  Translate: Position the ventricle centered in origin  Use “Source  Plane” as guide
File  Save Data  Save edited STL file
ParaView:

## Slide 12
Patient Specific
ModelFLOWs
Cardiac
Point Classification
Integration
1
1
2
2
3
3
4
4
STL Generation
More displacement when close to apex.
Iterative algorithm to fit volume.
Displacement following normal of elements.

## Slide 13
Patient Specific
ModelFLOWs
Cardiac
1. Load Geometry
Read STL file
Scale & extract point and connectivity data
Compute initial volume and face normals.
2. Classify Vertices
Detect and categorize vertices based on geometric conditions
3. Process Flow Rate Data
Read flow rate data
Interpolate flow rate data
Adjust flow rates to correct volume differences between systole and diastole.
4. Calculate Volume Variations
Define time steps for STL generation (nS).
Compute volume variations by integrating flow rate chart.
5. Generate STL Files
For each time step:
Calculate scaling factors for the ventricle's dimensions.
Adjust vertex displacements iteratively to match target volumes.
Write new geometry to STL file.
6. Prepare Inlet and Outlet Data
Derive inlet velocities and outlet flow rates from flow data.
Write results to CSV files.

## Slide 14
ModelFLOWs
Cardiac
Ideal
Patient Specific

## Slide 15
ModelFLOWs
Cardiac
https://modelflows.github.io/modelflowsapp/cardiacpathologydetection/
Any questions?
Look us up in our website: