## Slide 1
Tutorial: Star-CCM+ CFD
Eneko Lazpita
ModelFLOWs
Cardiac

## Slide 2
ModelFLOWs
Cardiac
Step 0: Prerequisites
Matlab with STL management packages.
Star-CCM+
STL files in end systole and in end diastole (max. and min. volumes)
Step 0.1: Load given .sim file
Setup of this tutorial done.
Step 0.2: Run create_necessary_files.m
We create the initial scaled mesh (if necessary) and the tables we need for boundary conditions: inlet, outlet, wall movement.

## Slide 3
ModelFLOWs
Cardiac
Geometry
Step 1.1: Load Geometry
Create geometry using Geometry  3D-CAD Models  New
Right click in 3D-CAD Model 1  Import -> CAD Model  Select your scaled initial mesh.
Close 3D-CAD

## Slide 4
ModelFLOWs
Cardiac
Step 1.2: Create Part & Boundaries
Inside the Body Groups Created right click on your body  New Geometry Part…  OK
Rename Part: Ventricle
Geometry  Parts  Right click in Ventricle  Repair Surface…  OK
Select boundary zone (double left click if your geometry has sharp edges around)
Right click on selected surface -> Edit Selected: Part Surface(s)  Modify to New…  Introduce boundary name (Inlet, Outlet, Wall)
Close
Geometry

## Slide 5
ModelFLOWs
Cardiac
Step 2.1: Create Continua
Right click in Continua  New Physics Continuum
Rename Physics 1 to “Blood”  Right click on Blood  Select Models…
  Three-Dimensional
  Liquid  Density: & Dynamic Viscosity:
  Constant Density (Incompressible Flow)
  Coupled Flow  Implicit, 2nd order
  Implicit Unsteady
  Laminar
  Wall Distance  Implicit Tree
  Solution Interpolation
Simulation Setup

## Slide 6
ModelFLOWs
Cardiac
Step 2.2: Create Region
Right click in Geometry  Parts  “Your body name”  Set New Region…  Introduce name “ Ventricle”
Regions  Ventricle  Right click in Boundaries  New
Rename boundary; Select corresponding Part Surface; Choose Type
  Inlet: type Velocity Inlet Physics Values  Introduce velocity profile (explained next)
  Outlet: type Outlet  Physics Conditions  Mass Flow Specification  Mass Flow Rate  Physics Values  Introduce mass flow profile (explained next)
  Wall: type Wall
Simulation Setup

## Slide 7
ModelFLOWs
Cardiac
Step 2.3: Import Data Tables
Simulation Setup
Tools  Right click in Tables  New Table  File Table Load:
  XYZ_displacement.csv
  Incremental_VolumeVariation_DT-%.csv
  InletVelocity_DT-%.csv
  OutletFlowRate_DT-%.csv
Tools  Right click in Field Functions  New  Scalar:
  Change function name: Inlet_Velocity, Outlet_FlowRate
  Introduce dimensions: [Velocity 1], [Length 3, Time -1]
  Interpolate tables: interpolateTablePeriodic(@Table("InletVelocity_DT-5e-04"), “t", LINEAR, “velin", ${Time},1,0) interpolateTablePeriodic(@Table(“OutletFlowRate_DT-5e-04"), “t", LINEAR, “fRout", ${Time},1,0)
Right click in Reports  New  User  Expression
  Change function name: Displacement_Interpolation
  Introduce dimensions: [Length 1]
  Interpolate tables: interpolateTablePeriodic(@Table("Incremental_VolumeVariation_DT-5e-04"), "t", LINEAR, "dVol", ${Time},1,0)

## Slide 8
ModelFLOWs
Cardiac
Step 2.4: Define Inlet & Outlet BCs
Simulation Setup
Tools  Right click in Parameters  New  Scalar:
  Define necessary parameters: R_Inlet = 0.012 m; C_Inlet = 0.006 m
Tools  Right click in Field Functions  New  Scalar:
  Define inlet radial coordinate: Inlet_RadialCoordinate = sqrt(pow($${Position}[0]+${C_inlet},2)+pow($${Position}[2],2))
  Define BC profiles: Inlet_Velocity_Tanh = 1.0745 * tanh(5 * (1 - ${Inlet_RadialCoordinate}/${R_Inlet}) ) * ${Inlet_Velocity} Outlet_MassFlowRate = ${Outlet_FlowRate} * ${Density}
Regions  Ventricle  Boundaries  Inlet  Physics Values  Velocity Magnitude
  Field Function  Inlet_Velocity_Tanh
Regions  Ventricle  Boundaries  Outlet  Physics Values  Mass Flow Rate
  Field Function  Outlet_MassFlowRate

## Slide 9
ModelFLOWs
Cardiac
Step 3.1: Specify Motion
Moving Wall
Tools  Right click in Motions  New  Morphing:
  Morpher Order  Regionwise
  Morpher Method  RBF
Tools  Right click in Data Mappers  New Data Mapper  Tabular Data Mapper:
  Source Table  XYZ_displacement.csv
  Source: Data  Select: Displacement[i], Displacement[j], Displacement[k]
  Target Specifications  Surface 1  Target Entities: Regions Ventricle  Boundaries  Wall
Tools  Data Mappers  Right click in Tabular Data Mapper 1  Map Data
Tools  Right click in Field Functions  New  Vector: Morpher_Entry = ${Displacement_Interpolation} * [${MappedVertexDisplacement[i]},${MappedVertexDisplacement[j]},${MappedVertexDisplacement[k]}]

## Slide 10
ModelFLOWs
Cardiac
Step 3.2: Specify Motion
Moving Wall
Right click in Monitors  New Monitor  Field Sum
  Rename: Sum_Displacement_X, Sum_Displacement_Y, Sum_Displacement_Z
  Parts: Ventricle  Wall
  Field Function: Morpher_Entry[i], Morpher_Entry[j], Morpher_Entry[k]
Tools  Right click in Field Functions  New  Vector: MorphSurfaceMesh_Entry = [${Sum_Displacement_XMonitor},${Sum_Displacement_YMonitor},${Sum_Displacement_ZMonitor}]

## Slide 11
ModelFLOWs
Cardiac
Step 3.3: Prepare Moving Wall Boundary
Moving Wall
Regions  Ventricle  Physics Values  Motion Specification  Motion: Morphing
Regions  Ventricle  Boundaries  Wall
  Physics Conditions  Morpher Specification: Displacement
  Physics Conditions  Morpher Displacement Specification: Incremental
  Physics Values  Morpher Incremental Linear Displacement  Field Function: Morpher_Entry
Morphing
Displacement
Incremental
Field Function: Morpher_Entry

## Slide 12
ModelFLOWs
Cardiac
Step 4.1: Automated Mesh
Geometry  Right click in Operations  New  Mesh  Automated Mesh
  Surface Remesher
  Tetrahedral Mesher
  Prism Layer Mesher
Automated Mesh  Default Controls define:
  Base Size
  Volume Growth Rate
  Prism Layer Controls (5 layers)
  Core Mesh Optimization (5 cycles, 0.8 threshold)
Automated Mesh  Mesher Execution Mode  Parallel
Meshing

## Slide 13
ModelFLOWs
Cardiac
Step 4.2: Morph Surface Mesh
Geometry  Right click in Operations  New  Surface Preparation  Morph Surface Mesh
  Input Parts  Ventricle
  Displacement Field  MorphSurfaceMesh_Entry
  Part Surfaces Mode  Include part surfaces
  Input Part Surfaces  Wall
Tab: Mesh  Generate Volume Mesh
Meshing

## Slide 14
Tools  Right click in Parameters  New  Scalar: Time_Step = 0.001 s
Solvers  Implicit Unsteady:
  Time-Step: ${Time_Step}
  Temporal Discretization: 2nd-order
Solvers  Mesh Morpher:
  Check: Morph At Initialization; Morph From Zero; Recompute Interfaces; Boundary Layer Morphing; Morph At Inner Iterations
Solvers  Coupled Implicit:
  CFL Control Method: Automatic
  Automatic CFL  Initial CFL: 1.0 Minimum CFL: 0.1 Maximum CFL: 10.0
ModelFLOWs
Cardiac
Step 5.1: Solver Methods & Controls
Meshing

## Slide 15
ModelFLOWs
Cardiac
Step 5.2: Automatic Export
Tab: File  Auto Export
  File Format: CGNS
  Base Name: solution
  Export Directory: solution
  Separator: _
  Scalar Functions: Density, Pressure
  Vector Functions: Velocity, Vorticity
  Regions: Ventricle
  Boundaries: Inlet, Outlet, Wall
  Update: Enabled Trigger: Time Step Frequency: 20

## Slide 16
ModelFLOWs
Cardiac
Step 5.3: Initialization & Run
Tools  Right click in Parameters  New  Scalar: T_Period = 0.001 s
Continua  Blood  Initial Conditions:
  Pressure = 0 Pa
  Velocity = [0.0, 0.0, 0.0] m/s
Stopping Criteria  Maximum Inner Iterations: (Enabled)
  Maximum Inner Iterations: 30
  Logical Rule: And
Stopping Criteria  Maximum Physical Time: (Enabled)
  Maximum Physical Time: 5 * ${T_Period}
  Logical Rule: And

## Slide 17
ModelFLOWs
Cardiac
Step 5.4: Initialization & Run
Tools  Data Mappers  Right click in Tabular Data Mapper 1  Map Data
Tab: Solution  Initialize Solution
Tab: Solution  Run
Everytime we Clear Solution or Restart Simulation, it is necessary to Map Data, Initialize and then Run

## Slide 18
ModelFLOWs
Cardiac
Vortex ring formation, tilting, second smaller ring and outflow
Two swirls in both E and A waves of diastole and outflow in systole
Big recirculation in ventricle center, down to the apex.
Q-Criterion
Vorticity
Velocity

## Slide 19
ModelFLOWs
Cardiac
https://modelflows.github.io/modelflowsapp/cardiacpathologydetection/
Any questions?
Look us up in our website: